## Slide 1: Computer Vision
Cameras, Lenses and Sensors

## Slide 2: Cameras, lenses and sensors
Camera Models
  Pinhole Perspective Projection
  Affine Projection
Camera with Lenses
Sensing
The Human Eye

## Slide 3
Images are two-dimensional patterns of brightness values.
They are formed by the projection of 3D objects.
Figure from US Navy Manual of Basic Optics and Optical Instruments, prepared by Bureau of
Naval Personnel. Reprinted by Dover Publications, Inc., 1969.

## Slide 4
Animal eye:
a long time ago.
Pinhole perspective projection: Brunelleschi, XVth Century.
Camera obscura: XVIth Century.
Photographic camera:
Niepce, 1816.

## Slide 5: Pinhole Cameras

## Slide 6: Distant objects appear smaller

## Slide 7: Parallel lines meet
vanishing point

## Slide 8: Vanishing Points
each set of parallel lines (=direction) meets at a different point
  The vanishing point for this direction
Sets of parallel lines on the same plane lead to collinear vanishing points.
  The line is called the horizon for that plane
Good ways to spot faked images
  scale and perspective don’t work
  vanishing points behave badly
  supermarket tabloids are a great source.

## Slide 9: Geometric properties of projection
Points go to points
Lines go to lines
Planes go to whole image
or half-plane
Polygons go to polygons
Degenerate cases:
  line through focal point yields point
  plane through focal point yields line

## Slide 10
Pinhole Perspective Equation
C’: image center
OC’: optical axis
OP’=lOP  x’=lx, y’=ly, z’=lz
A point P(x,y,z) and its projection onto the image plane p(x’,y’,z’). z’=f’ by definition

## Slide 11
Affine projection models:
Weak perspective projection
is the magnification.
When the scene depth is small compared its distance from the Camera, m can be taken constant: weak perspective projection.

## Slide 12
Affine projection models:
Orthographic projection
When the camera is at a
(roughly constant) distance
from the scene, take m=1.

## Slide 13: Limits for pinhole cameras
Notes: C 的入光亮也變少變更案
Diffraction ＝ 繞射

## Slide 14: Size of pinhole
Pinhole too big –many directions are averaged, blurring the image
Pinhole too small- diffraction effects blur the image
Generally, pinhole cameras are dark, because a very small set of rays from a particular point hits the screen.

## Slide 15
Camera obscura + lens


## Slide 16
Lenses
Snell’s law
n1 sin a1 = n2 sin a2
Descartes’ law

## Slide 17
Paraxial (or first-order) optics
Snell’s law:
n1 sin a1 = n2 sin a2
Small angles:
n1 a1  n2a2
入射角 = alph1 + beta

## Slide 18
Thin Lenses
spherical lens surfaces; incoming light  parallel to axis; thickness << radii; same refractive index on both sides

## Slide 19
Thin Lenses
http://www.phy.ntnu.edu.tw/java/Lens/lens_e.html

## Slide 20
Thick Lens
For large angles, use a third-order Taylor expansion of the sine function:

## Slide 21
The depth-of-field


## Slide 22
The depth-of-field

yields
Similar formula for
相似形
得到

## Slide 23
The depth-of-field
decreases with d, increases with Z0

strike a balance between incoming light and
sharp depth range

## Slide 24
Deviations from the lens model
3 assumptions :
1. all rays from a point are focused onto 1 image point
2. all image points in a single plane
3. magnification is constant
deviations from this ideal are aberrations


## Slide 25: Aberrations
geometrical : small for paraxial rays, study through 3rd order optics
chromatic : refractive index function of wavelength

## Slide 26
Geometrical aberrations
spherical aberration
astigmatism
distortion
coma
aberrations are reduced by combining lenses


## Slide 27
Spherical aberration
rays parallel to the axis do not converge
outer portions of the lens yield smaller focal lengths


## Slide 28: Astigmatism
Different focal length for inclined rays

## Slide 29: Distortion
magnification/focal length different
for different angles of inclination
Can be corrected! (if parameters are know)
pincushion
(tele-photo)
barrel
(wide-angle)

## Slide 30: Coma
point off the axis depicted as comet shaped blob

## Slide 31
Chromatic aberration
rays of different wavelengths focused
in different planes
cannot be removed completely
sometimes achromatization is achieved for
more than 2 wavelengths


## Slide 32
Vignetting
The shaded part of the beam never reaches the second lens. Additional apertures and stops in a lens further contribute to vignetting.

## Slide 33
Photographs
(Niepce,
“La Table Servie,” 1822)
Milestones:
Daguerreotypes (1839)
Photographic Film (Eastman,1889)
Cinema (Lumière Brothers,1895)
Color Photography
(Lumière Brothers, 1908)
Television
(Baird, Farnsworth, Zworykin, 1920s)
CCD Devices (1970)
more recently CMOS
Collection Harlingue-Viollet.

## Slide 34
Cameras
we consider 2 types :

1. CCD
2. CMOS

## Slide 35
CCD
separate photo sensor at regular positions
no scanning
charge-coupled devices (CCDs)
area CCDs and linear CCDs
2 area architectures :
interline transfer and frame transfer
photosensitive
storage


## Slide 36: The CCD camera

## Slide 37: CMOS
Same sensor elements as CCD
Each photo sensor has its own amplifier
  More noise (reduced by subtracting ‘black’ image)
  Lower sensitivity (lower fill rate)
Uses standard CMOS technology
  Allows to put other components on chip
Foveon
4k x 4k sensor
0.18 process
70M transistors

## Slide 38: CCD vs. CMOS
Mature technology
Specific technology
High production cost
High power consumption
Higher fill rate (amount of pixel picture vs. space in between)
Blooming
Sequential readout
Recent technology
Standard IC technology
Cheap
Low power
Less sensitive
Per pixel amplification
Random pixel access
Smart pixels
On chip integration with other components

## Slide 39: Color cameras
We consider 3 concepts:
  Prism (with 3 sensors)
  Filter mosaic
  Filter wheel
  … and X3

## Slide 40: Prism color camera
Separate light in 3 beams using dichroic prism
Requires 3 sensors & precise alignment
Good color separation

## Slide 41: Prism color camera

## Slide 42: Filter mosaic
Coat filter directly on sensor
Demosaicing (obtain full color & full resolution image)
Notes: 非真正的RGB
是用filter interpolate 出來的

## Slide 43: Filter wheel
Rotate multiple filters in front of lens
Allows more than 3 color bands
Only suitable for static scenes

## Slide 44: Prism vs. mosaic vs. wheel
Wheel
1
Good
Average
Low
Motion
3 or more
approach
# sensors
Separation
Cost
Framerate
Artefacts
Bands
Prism
3
High
High
High
Low
3
High-end
cameras
Mosaic
1
Average
Low
High
Aliasing
3
Low-end
cameras
Scientific applications

## Slide 45: New color CMOS sensor Foveon’s X3
better image quality
smarter pixels

## Slide 46
The Human Eye
Helmoltz’s
Schematic
Eye
Reproduced by permission, the American Society of Photogrammetry and
Remote Sensing. A.L. Nowicki, “Stereoscopy.” Manual of Photogrammetry,
Thompson, Radlinski, and Speert (eds.), third edition, 1966.

## Slide 47
The distribution of rods and cones across the retina
Reprinted from Foundations of Vision, by B. Wandell, Sinauer
Associates, Inc., (1995).  1995 Sinauer Associates, Inc.
Cones in the
fovea
Rods and cones in
the periphery
Reprinted from Foundations of Vision, by B. Wandell, Sinauer
Associates, Inc., (1995).  1995 Sinauer Associates, Inc.